Microwave Imager
Analysis of bandpass measurements of MWI channels 14-18
Calculation of virtual measurements
Comparison to calculated TB
Influence of integrated water vapor and clouds
MWI
Scientific Advisory Group Meeting
Nils Risse, Susanne Crewell, Mario Mech,
November 23, 2020
n.risse@uni-koeln.de

---
Agenda
- Introduction
- Data
  - Bandpass measurements
  - Atmospheric data
- Methods
- Results and Discussion
- Conclusions

---
Introduction
- Spectral sensitivity of 183 GHz MWI channels (MWI-14 to MWI-18)
- Is the bandpass effect depending on the climatic region?

---
Data: Bandpass measurements
- Frequency range: 175.322–191.302 GHz
- Resolution: 15 MHz
- No data at 183.312 GHz \pm 55 MHz
- Number of measurements: 1060

---
Data: Radiosonde
- Daily 12 UTC radiosonde data of year 2019
  - Ny Alesund (Arctic); Essen (Mid-latitude)
    Barbados (Tropics); Singapore (Tropics)
  - Vertical profiles of pressure, temperature and humidity
    → “clear-sky” conditions
- Data availability
  - Ny Alesund: 96.7 %
  - Essen: 98.9 %
  - Singapore: 98.6 %
  - Barbados: 73.4 %

---
Methods: Radiative transfer simulation
- Model: Passive and Active Microwave TRAnsfer (PAMTRA, Mech et al. 2020)
  - Brightness temperature at every frequency (vertical polarization)
  - 733 km nadir view
- Input parameters:
  - Atmospheric state: pressure, temperature and relative humidity as function of height, cloud parameters
  - Add source of atmospheric state

---
Methods: Calculation of virtual MWI measurement
- Normalize bandpass measurement at frequency i:
- Virtual MWI measurement is then given by:
s_{norm, i}(\nu) = \frac{s_i(\nu)}{\sum_{i}^{N} s_i(\nu)}
T_{B, MWI} = \sum_{i}^{} s(f_i) T_{B, PAM}(f_i)

---
Results: Radiosonde profiles
- Radiosonde profile
- TODO: show mean seasonal profiles?

---
Results: PAMTRA simulation for radiosondes
- TODO: mean profiles?
- else: take examples

---
Standard atmosphere

---
Results: Seasonal differences (center frequency)
- Arctic (Ny Alesund)
  - ΔTB very variable with annual cycle
- Mid-latitude (Essen)
  - lower variability than Arctic, small annual cycle
- Tropics (Singapore)
  - lowest ΔTB of all locations (channel 14-17)
- Channel 14: lowest ΔTB for each location
- Channel 18: ΔTB below 0 for every location

---
Results: Seasonal differences (frequency at bandwidth)
- Arctic (Ny Alesund)
  - ΔTB extremely variable with annual cycle
- Mid-latitude (Essen)
  - similar ΔTB for all channels
- Tropics (Singapore)
  - lowest ΔTB of all locations (channel 14-17)
- Channel 14: lowest ΔTB for each location
- Channel 18: ΔTB below 0 for every location

---
Results: Seasonal differences (center frequency and bandwidth f)
- Arctic (Ny Alesund)
  - ΔTB very variable with annual cycle
- Mid-latitude (Essen)
  - lower variability than Arctic, small annual cycle
- Tropics (Singapore)
  - lowest ΔTB of all locations (channel 14-17)
- Channel 14: lowest ΔTB for each location
- Channel 18: ΔTB below 0 for every location

---
Results: Influence of perturbed SRF
- Summary of 1000 realizations of perturbed SRF
- Average ΔTB does not change (not shown)
- Standard deviation of ΔTB increases with increasing perturbation
- Strongest increase for channel 18
- TODO: add fig that shows perturbation series
- TODO: change to bw center

---
Results: Influence of increased sampling interval
- Relative change of ΔTB with respect to decreasing number of measurement points
- Increase of sampling interval to 30 GHz has nearly no influence
- A further increase leads to fluctiating differences
- TODO: change to bw center
- TODO: add fig that shows perturbation series

---
Results: Influence of column-integrated Water Vapor
- IWV explains major parts of deviation for channels 14 to 17
- Variance highest for channel 18
- Comparison with central frequency shows lowest variability (left column)
- TODO: update plot only for 2019 profiles
- TODO: add wv plots for profiles

---
Results: Cloud effects

---
Conclusion

---
Outlook
- Correction functions can be defined for clear-sky conditions, given a priori information about integrated water vapor

---
Literature
Radiosonde data: University of Wyoming