Agenda
- Introduction
- Data
  - Bandpass measurements
  - Atmospheric data
- Methods
- Results and Discussion
- Conclusions

---
Introduction
- Spectral sensitivity of 183 GHz MWI channels (MWI-14 to MWI-18)
- Is the bandpass effect depending on the climatic region?

---
Bandpass measurements
- Frequency range: 175.322–191.302 GHz
- Resolution: 15 MHz
- No data at 183.312 GHz \pm 55 MHz
- Number of measurements: 1060

---
Methods: Radiative transfer simulation
- Model: Passive and Active Microwave TRAnsfer (PAMTRA, Mech et al. 2020)
  - Brightness temperature at every frequency (vertical polarization)
  - 733 km nadir view
- Input parameters:
  - Atmospheric state: pressure, temperature and relative humidity as function of height, cloud parameters
  - Add source of atmospheric state

---
Methods: Calculation of virtual MWI measurement
- Normalize bandpass measurement at frequency i:
- Virtual MWI measurement is then given by:
s_{norm, i}(\nu) = \frac{s_i(\nu)}{\sum_{i}^{N} s_i(\nu)}
T_{B, MWI} = \sum_{i}^{} s(f_i) T_{B, PAM}(f_i)